## Slide 1
Networking Lab (Final)
Assignment
Shanto Mariam University of Creative Technology
Department: CSE
CSE-3286: Networking Lab [A]
Submitted to:
Dr. Md. Rabiul Islam, Professor,
Department of CSE & CSIT SMUCT
Prepared by:
Antor Hawlader
ID: 222071024
Dept: CSE
Batch: 30th
8th Semester

## Slide 3
Lab 1 - LAN

## Slide 4
Lab 2 - WAN

## Slide 5
Router>enable
Router#configure terminal
Router(config)#interface fa0/0
Router(config-if)#ip address 192.168.10.1 255.255.255.0
Router(config-if)#no shutdown
Router Configuration
Router>enable
Router#configure terminal
Router(config)#interface se2/0
Router(config-if)#ip address 10.10.10.1 255.255.255.0
Router(config-if)#clock rate 64000
Router(config-if)#no shutdown
Router Configuration (Serial)
Serial DCE
Router>enable
Router#show ip route
Router#show running-config
Router#show startup-config
Router#copy running-config startup-config
More
Router>enable
Router#configure terminal
Router(config)#ip route 192.168.20.0 255.255.255.0 se2/0
IP Route Configuration (Router0)
Router>enable
Router#configure terminal
Router(config)#ip route 192.168.10.0 255.255.255.0 se3/0
IP Route Configuration (Router1)
Router0
Router1
Router>enable
Router#configure terminal
Router(config)#interface fa0/0
Router(config-if)#ip address 192.168.20.1 255.255.255.0
Router(config-if)#no shutdown
Router Configuration
Router>enable
Router#configure terminal
Router(config)#interface se3/0
Router(config-if)#ip address 10.10.10.2 255.255.255.0
Router(config-if)#no shutdown
Router Configuration (Serial)

## Slide 6
CIDR | Subnet Mask | Hosts (Usable)
/1 | 128.0.0.0 | 2,147,483,646
/2 | 192.0.0.0 | 1,073,741,822
/3 | 224.0.0.0 | 536,870,910
/4 | 240.0.0.0 | 268,435,454
/5 | 248.0.0.0 | 134,217,726
/6 | 252.0.0.0 | 67,108,862
/7 | 254.0.0.0 | 33,554,430
/8 | 255.0.0.0 | 16,777,214
/9 | 255.128.0.0 | 8,388,606
/10 | 255.192.0.0 | 4,194,302
/11 | 255.224.0.0 | 2,097,150
/12 | 255.240.0.0 | 1,048,574
/13 | 255.248.0.0 | 524,286
/14 | 255.252.0.0 | 262,142
/15 | 255.254.0.0 | 131,070
/16 | 255.255.0.0 | 65,534
/17 | 255.255.128.0 | 32,766
/18 | 255.255.192.0 | 16,382
/19 | 255.255.224.0 | 8,190
/20 | 255.255.240.0 | 4,094
/21 | 255.255.248.0 | 2,046
/22 | 255.255.252.0 | 1,022
/23 | 255.255.254.0 | 510
/24 | 255.255.255.0 | 254
/25 | 255.255.255.128 | 126
/26 | 255.255.255.192 | 62
/27 | 255.255.255.224 | 30
/28 | 255.255.255.240 | 14
/29 | 255.255.255.248 | 6
/30 | 255.255.255.252 | 2
/31 | 255.255.255.254 | 0*
/32 | 255.255.255.255 | 0
Lab 3 - Subnetting hand calculation

## Slide 7
Solution of the problem: 172.17.0.0 / 20
Step 1: Sort (Descending order) the number of subnets according to their requirement
1st -- subnet, EEE Department LAN => 210 + 2 = 212 - (28) /24
2nd -- subnet, CSE Department LAN => 112 + 2 = 114 - (27) /25
3rd -- subnet, ETE Department LAN => 64 + 2 = 66 - (27) /25
Step 2: Step 3: 212 <= 2N
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | 
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Network EEE | 172.17.0.0 / 24
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1st Host of EEE | 172.17.0.1 / 24
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | Last Host of EEE | 172.17.0.254 / 24
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Broadcast EEE | 172.17.0.255 / 24
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Network CSE | 172.17.1.0 / 25
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1st Host of CSE | 172.17.1.1 / 25
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | Last Host of CSE | 172.17.1.126 / 25
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Broadcast CSE | 172.17.1.127 / 25
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Network ETE | 172.17.1.128 / 25
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1st Host of ETE | 172.17.1.129 / 25
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | Last Host of ETE | 172.17.1.254 / 25
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | Broadcast ETE | 172.17.1.255 / 25
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Network CSE-ETE | 172.17.2.0 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1st Host of CSE-ETE | 172.17.2.1 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | Last Host of CSE-ETE | 172.17.2.2 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | Broadcast CSE-ETE | 172.17.2.3 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | Network CSE-EEE | 172.17.2.4 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1st Host of CSE-EEE | 172.17.2.5 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | Last Host of CSE-EEE | 172.17.2.6 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | Broadcast CSE-EEE | 172.17.2.7 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | Network EEE-ETE | 172.17.2.8 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1st Host of EEE-ETE | 172.17.2.9 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | Last Host of EEE-ETE | 172.17.2.10 / 30
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | Broadcast EEE-ETE | 172.17.2.11 / 30
4th -- Point to point link between CSE and ETE => 2 + 2 = 4 - (22) /30
5th -- Point to point link between CSE and EEE => 2 + 2 = 4 - (22) /30
6th -- Point to point link between EEE and ETE => 2 + 2 = 4 - (22) /30

## Slide 8
Subnet Name | Needed Size | Allocated Size | Network Address | Mask | Assignable Range | Broadcast Address
EEE | 210 | 254 | 172.17.0.0 / 24 | 255.255.255.0 | 172.17.0.1 - 172.17.0.254 | 172.17.0.255
CSE | 112 | 126 | 172.17.1.0 / 25 | 255.255.255.128 | 172.17.1.1 - 172.17.1.126 | 172.17.1.127
ETE | 64 | 126 | 172.17.1.128 / 25 | 255.255.255.128 | 172.17.1.129 - 172.17.1.254 | 172.17.1.255
CSE-ETE | 2 | 2 | 172.17.2.0 / 30 | 255.255.255.252 | 172.17.2.1 - 172.17.2.2 | 172.17.2.3
CSE-EEE | 2 | 2 | 172.17.2.4 / 30 | 255.255.255.252 | 172.17.2.5 - 172.17.2.6 | 172.17.2.7
EEE-ETE | 2 | 2 | 172.17.2.8 / 30 | 255.255.255.252 | 172.17.2.9 - 172.17.2.10 | 172.17.2.11

## Slide 9
Lab 4 - Subnetting packet tracer activity

## Slide 10
Router>enable
Router#configure terminal
Router(config)#interface fa0/0
Router(config-if)#ip address 172.17.0.1 255.255.255.0
Router(config-if)#no shutdown
Router Configuration
Router(config)#interface se2/0
Router(config-if)#ip address 172.17.2.6 255.255.255.252
Router(config-if)#clock rate 64000
Router(config-if)#no shutdown
Router(config-if)#exit
Router Configuration (Serial se2/0)
Serial DCE
Router(config)#ip route 172.17.1.0 255.255.255.128 se2/0
Router(config)#ip route 172.17.1.128 255.255.255.128 se3/0
IP Route Configuration
Router-PT R0 (EEE)
Router(config)#interface se3/0
Router(config-if)#ip address 172.17.2.9 255.255.255.252
Router(config-if)#no shutdown
Router Configuration (Serial se3/0)
Router>enable
Router#configure terminal
Router(config)#interface fa0/0
Router(config-if)#ip address 172.17.1.1 255.255.255.0
Router(config-if)#no shutdown
Router Configuration
Router(config)#interface se2/0
Router(config-if)#ip address 172.17.2.1 255.255.255.252
Router(config-if)#clock rate 64000
Router(config-if)#no shutdown
Router(config-if)#exit
Router Configuration (Serial se2/0)
Serial DCE
Router(config)#ip route 172.17.0.0 255.255.255.0 se2/0
Router(config)#ip route 172.17.1.128 255.255.255.128 se3/0
IP Route Configuration
Router-PT R2 (CSE)
Router(config)#interface se3/0
Router(config-if)#ip address 172.17.2.5 255.255.255.252
Router(config-if)#no shutdown
Router Configuration (Serial se3/0)
Router>enable
Router#configure terminal
Router(config)#interface fa0/0
Router(config-if)#ip address 172.17.1.129 255.255.255.0
Router(config-if)#no shutdown
Router Configuration
Router(config)#interface se2/0
Router(config-if)#ip address 172.17.2.10 255.255.255.252
Router(config-if)#clock rate 64000
Router(config-if)#no shutdown
Router(config-if)#exit
Router Configuration (Serial se2/0)
Serial DCE
Router(config)#ip route 172.17.0.0 255.255.255.0 se2/0
Router(config)#ip route 172.17.1.0 255.255.255.128 se3/0
IP Route Configuration
Router(config)#interface se3/0
Router(config-if)#ip address 172.17.2.2 255.255.255.252
Router(config-if)#no shutdown
Router Configuration (Serial se3/0)
Router-PT R1 (ETE)

## Slide 11
Lab 5 - Wireless LAN (WLAN)

## Slide 14
Lab 6 - DHCP

## Slide 15
Router>enable
Router#configure terminal
Router(config)#interface fa0/0
Router(config-if)#ip address 192.168.10.1 255.255.255.0
Router(config-if)#no shutdown
Router Configuration
Router(config)#ip dhcp excluded-address 192.168.10.1 192.168.10.10
Router(config)#ip dhcp excluded-address 192.168.10.254
Router(config)#ip dhcp pool LAN-POOL-1
Router(dhcp-config)#network 192.168.10.0 255.255.255.0
Router(dhcp-config)#default-router 192.168.10.1
Router#copy running-config startup-config
Router Configuration (DHCP)
Router0

## Slide 16
Lab 7 - VLAN

## Slide 18
Switch1
Switch#show vlan brief
More
Router>enable
Router#configure terminal
Switch(config)#interface range fa1/1, fa2/1, fa3/1
Switch(config-if)#switchport mode access
Switch(config-if)#no shutdown
User ports of S1 and S2 are enabled as access ports
Switch(config)#vlan 10
Switch(config-vlan)#name faculty
Switch(config)#vlan 20
Switch(config-vlan)#name students
Switch(config)#vlan 30
Switch(config-vlan)#name guest
Switch(config)#vlan 99
Switch(config-vlan)#name management
Switch(config-vlan)#end
Create VLANs on S0, S1, and S2
Switch(config)#interface fa1/1
Switch(config-if)#switchport access vlan 10
Switch(config-if)#no shutdown
Switch(config)#interface fa2/1
Switch(config-if)#switchport access vlan 20
Switch(config-if)#no shutdown
Switch(config)#interface fa3/1
Switch(config-if)#switchport access vlan 30
Switch(config-if)#no shutdown
Assign switch ports to VLANs on S1 and S2
Switch(config)#interface fa0/1
Switch(config-if)#switchport mode trunk
Switch(config-if)#switchport trunk native vlan 99
Switch(config-if)#no shutdown
Configure trunking and native VLAN between the switches
Configure the PCs with appropriate IP addresses
Switch(config)#interface vlan 99
Switch(config-if)#ip address 117.17.99.12 255.255.255.0
Switch(config-if)#no shutdown
Assign the management VLAN on all switches
Switch2
Router>enable
Router#configure terminal
Switch(config)#interface range fa1/1, fa2/1, fa3/1
Switch(config-if)#switchport mode access
Switch(config-if)#no shutdown
User ports of S1 and S2 are enabled as access ports
Switch(config)#vlan 10
Switch(config-vlan)#name faculty
Switch(config)#vlan 20
Switch(config-vlan)#name students
Switch(config)#vlan 30
Switch(config-vlan)#name guest
Switch(config)#vlan 99
Switch(config-vlan)#name management
Switch(config-vlan)#end
Create VLANs on S0, S1, and S2
Switch(config)#interface fa1/1
Switch(config-if)#switchport access vlan 10
Switch(config-if)#no shutdown
Switch(config)#interface fa2/1
Switch(config-if)#switchport access vlan 20
Switch(config-if)#no shutdown
Switch(config)#interface fa3/1
Switch(config-if)#switchport access vlan 30
Switch(config-if)#no shutdown
Assign switch ports to VLANs on S1 and S2
Switch(config)#interface fa0/1
Switch(config-if)#switchport mode trunk
Switch(config-if)#switchport trunk native vlan 99
Switch(config-if)#no shutdown
Configure trunking and native VLAN between the switches
Configure the PCs with appropriate IP addresses
Switch(config)#interface vlan 99
Switch(config-if)#ip address 117.17.99.13 255.255.255.0
Switch(config-if)#no shutdown
Assign the management VLAN on all switches
Switch0
Router>enable
Router#configure terminal
User ports of S1 and S2 are enabled as access ports
Switch(config)#vlan 10
Switch(config-vlan)#name faculty
Switch(config)#vlan 20
Switch(config-vlan)#name students
Switch(config)#vlan 30
Switch(config-vlan)#name guest
Switch(config)#vlan 99
Switch(config-vlan)#name management
Switch(config-vlan)#end
Create VLANs on S0, S1, and S2
Assign switch ports to VLANs on S1 and S2
Switch(config)#interface range fa0/1, fa1/1
Switch(config-if)#switchport mode trunk
Switch(config-if)#switchport trunk native vlan 99
Switch(config-if)#no shutdown
Configure trunking and native VLAN between the switches
Configure the PCs with appropriate IP addresses
Switch(config)#interface vlan 99
Switch(config-if)#ip address 117.17.99.11 255.255.255.0
Switch(config-if)#no shutdown
Assign the management VLAN on all switches

## Slide 19
Lab 8 - Inter-VLAN

## Slide 20
Lab 9 - Switch Port Security

## Slide 21
Lab 10 - OSPF

## Slide 22
Lab 11 - Static and default route

## Slide 23
Lab 12 - NAT (Static)

## Slide 24
Lab 13 - NAT (Dynamic)

## Slide 25
Lab 14 - Link Aggregation

## Slide 26
Lab 15 - Console, Telnet and SSH Configuration